Data packet protocol

Data packet consists of two parts: header and data.
Header:
Byte position	Description
packet[0]	Message type. Can be one of WIFI_CONFIG or MQTT_CONFIG.
packet[1]	Data length MSB byte
packet[2]	Data length LSB byte

Table 1. Structure of header.

Bytes from packet[3] are data that represents configs. To get data size you need to calculate it: size = packet[1] << 8 | packet[2].
Bytes starting from packet[3] to packet[size-1] are payload. Wifi configuration consists of two data fields: wifi ssid and wifi password. To distinguish between ssid and password we use symbol ‘\n’ as separator. So, if you want to parse packet – skip first 3 bytes and split packet by separator.

General structure of wifi config packet:
WIFI_CONFIG	Size MSB	Size LSB	SSID	SEPARATOR	PASSWORD

General structure of mqtt config packet:
MQTT_CONFIG	Size MSB	Size LSB	Server name	SEPARATOR	Port	SEPARATOR	User	SEPARATOR	Password

Table 2: Constants and description
Constant	Value	Description
WIFI_CONFIG	3	Indicates that current packet is for wifi configuration.
MQTT_CONFIG	4	Indicates that current packet is for mqtt configuration.
SEPARATOR	‘\n’	Byte used for splitting payload.
HEADER_SIZE	3	Size of header.
HEADER_TYPE_INDEX	0	Index of byte that represents payload type(WIFI_CONFIG or MQTT_CONFIG).
HEADER_LEN_MSB_INDEX	1	MSB byte of payload size
HEADER_LEN_LSB_INDEX	2	LSB byte of payload size.
WIFI_ERROR	10	Error code. ESP32 module sends this value if connection to WiFi failed.